## Slide 1
Katia Compagnoni
02nd December 2021
MOD_20_21 and other undo scenarios
Changes to Appendix O for Instruction Profiling and Bid Offer Acceptance Quantity Outcomes in a Subset of Undo Scenarios

## Slide 2
  In four scenarios, expected to be relatively rare, the outcome in the system is different to that in rules;
  They refer to undo dispatch actions in Instruction Profiling, originally considered defects, but now classed as changes;
  The SEMC decision on Mod_27_18 requires SEMO to correct those non-compliances by fixing the systems;
  The vendor’s recent high level impact assessment states that each change is deemed very high cost and very high risk and will need individual detailed assessments;
  SEMO is proposing to request detailed impact assessments for three scenarios (two of which grouped) while changing the T&SC for scenario 2.
Subset of Undo Scenarios - Background

## Slide 3
Scenario 1 ‘SYNC with MWOF undo to level below MSG before reaching MSG’
Change to the system pending detailed impact assessment (grouped with Scenario 4):
  7 cases identified since Oct 2019 – 1 in 2019, 3 in 2020 and 3 in 2021
  one case of high materiality (approx. 800K) in 2020 all others low materiality but 2 unknown due to no IP profile
Scenario 2 ‘SYNC with DESY after MSG but before reaching Min On Time’
Modification to the Code (Mod_20_21) to align with the system:
  No cases identified since go live – not material
Scenario 3 ‘DESY with SYNC after reaching zero before Min Off Time’
Change to the system pending detailed Impact assessment:
  7 cases identified since go live - 1 in 2018, 1 in 2019, and 5 in 2021
  Materiality vary from >100€ to approximately 200K
Scenario 4 ‘SYNC with DESY before reaching MSG’
Change to the system pending detailed impact assessment (grouped with Scenario 1):
  2 case identified in 2018 and none since
  Materiality of 190K and 580K
Subset of Undo Scenarios - Summary

## Slide 4
Scenario 1 ‘SYNC with MWOF undo to level below MSG before reaching MSG’
Change to the system pending detailed impact assessment (grouped with Scenario 4):
  7 cases identified since Oct 2019 – 1 in 2019, 3 in 2020 and 3 in 2021
  one case of high materiality (approx. 800K) in 2020 all others low materiality but 2 unknown due to no IP profile
Scenario 2 ‘SYNC with DESY after MSG but before reaching Min On Time’
Modification to the Code(Mod_20_21) to align with the system:
  No cases identified since go live – not material
Scenario 3 ‘DESY with SYNC after reaching zero before Min Off Time’
Change to the system pending detailed Impact assessment:
  7 cases identified since go live - 1 in 2018, 1 in 2019, and 5 in 2021
  Materiality vary from >100€ to approximately 200K
Scenario 4 ‘SYNC with DESY before reaching MSG’
Change to the system pending detailed impact assessment (grouped with Scenario 1):
  2 case identified in 2018 and none since
  Materiality of 190K and 580K
Subset of Undo Scenarios - Summary

## Slide 5
SYNC to MSG with subsequent MWOF below MSG before reaching MSG
Scenario 1 – Intention of rules
time
MW
Min On Time
SYNC
Issue
FPN
SYNC
Effective

## Slide 6
SYNC to MSG with subsequent MWOF below MSG before reaching MSG
Scenario 1 – Intention of rules
time
MW
Min On Time
SYNC
Issue
FPN
SYNC
Effective
MWOF
MWOF

## Slide 7
SYNC to MSG with subsequent MWOF below MSG before reaching MSG
Scenario 1 – Intention of rules
time
MW
Min On Time
SYNC
Issue
FPN
SYNC
Effective
MWOF
PMWO

## Slide 8
SYNC to MSG with subsequent MWOF below MSG before reaching MSG
Scenario 1 – Happening in systems
time
MW
Min On Time
SYNC
Issue
FPN
SYNC
Effective
MWOF
MWOF

## Slide 9
SYNC to MSG with subsequent MWOF below MSG before reaching MSG
Profile will return to ‘normal’ with a MWOF > MSG following the heat state at the time of the new MWOF
Scenario 1 – Impacted area
time
MW
Min On Time
SYNC
Issue
FPN
SYNC
Effective
MWOF
PMWO

## Slide 10
SYNC and DESY before MSG
Scenario 4 – Intention of rules
time
MW
SYNC
Effective
Min On Time
SYNC
Issue
FPN

## Slide 11
SYNC and DESY before MSG
Scenario 4 – Intention of rules
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue

## Slide 12
SYNC and DESY before MSG
Scenario 4 – Intention of rules
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue
PDES
Min Off Time

## Slide 13
SYNC and DESY before MSG
Scenario 4 – Happening in systems
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue
PDES
Min Off Time

## Slide 14
SYNC and DESY before MSG
Scenario 4 – Impacted area
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue
PDES
Min Off Time

## Slide 15
Scenario 1 ‘SYNC with MWOF undo to level below MSG before reaching MSG’
Change to the system pending detailed impact assessment (grouped with Scenario 4):
  7 cases identified since Oct 2019 – 1 in 2019, 3 in 2020 and 3 in 2021
  one case of high materiality (approx. 800K) in 2020 all others low materiality but 2 unknown due to no IP profile
Scenario 2 ‘SYNC with DESY after MSG but before reaching Min On Time’
Modification to the Code (Mod_20_21) to align with the system:
  No cases identified since go live – not material
Scenario 3 ‘DESY with SYNC after reaching zero before Min Off Time’
Change to the system pending detailed Impact assessment:
  7 cases identified since go live - 1 in 2018, 1 in 2019, and 5 in 2021
  Materiality vary from >100€ to approximately 200K
Scenario 4 ‘SYNC with DESY before reaching MSG’
Change to the system pending detailed impact assessment (grouped with Scenario 1):
  2 case identified in 2018 and none since
  Materiality of 190K and 580K
Subset of Undo Scenarios - Summary

## Slide 16
SYNC and DESY after MSG before Min On Time
Scenario 2 – Intention of rules
FPN
time
MW
SYNC
Effective
Min On Time
SYNC
Issue

## Slide 17
SYNC and DESY after MSG before Min On Time
Scenario 2 – Intention of rules
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue

## Slide 18
SYNC and DESY after MSG before Min On Time
Scenario 2 – Intention of rules
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue
PDES
Min Off Time

## Slide 19
SYNC and DESY after MSG before Min On Time
Scenario 2 – Happening in systems
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue
PDES
PSYN
Min Off Time

## Slide 20
SYNC and DESY after MSG before Min On Time
Profile will return to ‘normal’ after PISP (pseudo instruction at the Imbalance Settlement Period boundary) which will close off Pseudo Instructions
Scenario 2 – Impacted area
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue
PDES
PSYN
Min Off Time

## Slide 21
Additional paragraph in the PSYN definition Appendix O.16 Table 3
  If a subsequent DESY Dispatch Instruction has an Instruction Effective Time which is between the Instruction Effective Time of a prior SYNC Dispatch Instruction and the Instruction Effective Time of the corresponding PSYN Pseudo Dispatch Instruction that would nominally be created, but after the time when the Physical Notification Instruction Profile for the SYNC Dispatch Instruction reaches the Registered Minimum Stable Generation, then the PSYN Pseudo Dispatch Instruction that would nominally be created for the corresponding SYNC Dispatch Instruction shall be created.
Scenario 2 - MOD_20_21 Proposed Legal Drafting

## Slide 22
Please note that an error in the Modification form shows changes referring to Appendix O.14 table 1:
  14. How the Instruction Codes and Instruction Combination Codes are used for the calculation of Physical Notification Instruction Profiles is described in Table 1.
While the paragraph on PSYN definition actually belongs to Appendix O.16 table 3:
  16. A Pseudo Dispatch Instruction shall not be created for a corresponding Dispatch Instruction where the System Operator issues a subsequent Dispatch Instruction with Instruction Effective Time at or before the time at which the first Target Instruction Level is reached.
Scenario 2 - MOD_20_21 correction for FRR

## Slide 23
Scenario 1 ‘SYNC with MWOF undo to level below MSG before reaching MSG’
Change to the system pending detailed impact assessment (grouped with Scenario 4):
  7 cases identified since Oct 2019 – 1 in 2019, 3 in 2020 and 3 in 2021
  one case of high materiality (approx. 800K) in 2020 all others low materiality but 2 unknown due to no IP profile
Scenario 2 ‘SYNC with DESY after MSG but before reaching Min On Time’
Modification to the Code (Mod_20_21) to align with the system:
  No cases identified since go live – not material
Scenario 3 ‘DESY with SYNC after reaching zero before Min Off Time’
Change to the system pending detailed Impact assessment:
  7 cases identified since go live - 1 in 2018, 1 in 2019, and 5 in 2021
  Materiality vary from >100€ to approximately 200K
Scenario 4 ‘SYNC with DESY before reaching MSG’
Change to the system pending detailed impact assessment (grouped with Scenario 1):
  2 case identified in 2018 and none since
  Materiality of 190K and 580K
Subset of Undo Scenarios - Summary

## Slide 24
DESY and SYNC after zero before Min Off Time
Scenario 3 – Intention of rules
FPN
time
MW
DESY
Min Off Time

## Slide 25
DESY and SYNC after zero before Min Off Time
Scenario 3 – Intention of rules
FPN
time
MW
DESY
SYNC
Effective
Min On Time
SYNC
Issue
Min Off Time

## Slide 26
DESY and SYNC after zero before Min Off Time
Scenario 3 – Intention of rules
FPN
time
MW
DESY
SYNC
Effective
SYNC
Issue
Min Off Time
PSYN
Min On Time

## Slide 27
DESY and SYNC after zero before Min Off Time
Scenario 3 – Happening in systems
FPN
time
MW
DESY
SYNC
Effective
SYNC
Issue
PDES
Min Off Time
PSYN
Min On Time

## Slide 28
DESY and SYNC after zero before Min Off Time
Profile will return to ‘normal’ after PISP (pseudo instruction at the Imbalance Settlement Period boundary) which will close off Pseudo Instructions
Scenario 3 – Impacted area
FPN
time
MW
DESY
SYNC
Effective
SYNC
Issue
PDES
Min Off Time
PSYN
Min On Time

## Slide 29
  SEMO propose 1 Modification to the T&SC and 3 system changes;
  Scenario 4 could be considered a subset requirement of Scenario 1 (subject to vendor approval);
  Until receiving vendor approval of the above, Mod_21_21 should be put on hold;
  Given the high level assessment, SEMO deem more beneficial a change the T&SC for Scenario 2 as it is the least impacting of the 4;
  The earliest implementation is Release K – spring 2023;
  Precedence to be given to bundled Scenarios 1 and 4;
  Resettlement back to 2018 only for existing upheld queries;
  The remaining period to be covered in scheduled M+4/13.
Subset of Undo Scenarios – Summary of proposed approach

## Slide 30
  All scenarios should require detailed Impact Assessment regardless of cost;
  All scenarios should require Modifications to the T&SC and no changes to the systems ;
  Both T&SC and system could be left unchanged with a regulatory acknowledgement of the non-compliance;
  Proposed changes to the T&SC could be made to Chapter H instead of Appendix O to maintain the original intent;
  Changes to the system could be implemented but applied only from an agreed cut off point;
  Others?
Subset of Undo Scenarios – Alternative approaches